## Slide 1
AquaGuard
AI-Powered Real-Time Urban Water Quality Monitoring
Degradation Prediction | Early Warning | Probable Cause Identification
AI Night Challenge 2026

## Slide 2
The Problem
2B+
people lack safe drinking water
485K
deaths/year from contaminated water
Hours
delay in current lab-based testing
>60%
false alarm rate in threshold systems
Current monitoring: periodic grab samples, lab results in hours to days
Threshold-based SCADA alarms: too many false positives, no prediction capability
No automated root-cause identification -- operators rely on experience
Gap: no early warning BEFORE water quality degrades to unsafe levels
Public health at risk: contamination events detected AFTER consumption

## Slide 3
Our Solution: End-to-End Architecture
Multi-Sensor Ingestion
pH, Turbidity, Chloramine Conductivity, THM, TDS 5-min intervals, 5 sites
Feature Engineering
279 features: Rolling stats, EWMA Derivatives, Lags Cyclical time encoding
ML Models (LightGBM)
Potability classifier Cause identifier Per-sensor forecasters
Risk Index & Alerts
WQRI 0-100 score Persistence + Hysteresis False alarm reduction
Streamlit Dashboard (5 Tabs)
Risk Overview: gauge + timeline + multi-site comparison
Sensor Trends: per-sensor charts with regulatory limits
Alerts Log: transition history with false alarm tracking
Root Cause: diagnosis panel with confidence + explanations
FastAPI Inference Service
POST /predict -- single reading prediction
WS /ws/stream -- WebSocket live demo streaming
GET /health -- system health check
Production-ready: async, CORS, schema validation

## Slide 4
Water Quality Risk Index (WQRI)
WQRI = EWMA( SUM(weight_i x deviation_score_i) / SUM(weight_i) ) score: 0-100
Sensor Weights (domain-driven)
Chloramine
0.22
Disinfectant loss = pathogen risk
Turbidity
0.20
Pathogen surrogate
THM
0.15
Carcinogenic byproduct
pH
0.12
Corrosion / scaling
Conductivity
0.10
Contamination proxy
Organic C
0.08
DBP precursor
TDS / Sulfate / Hardness
0.13
Secondary quality
Risk Scale & Alert Logic
0-30
EXCELLENT
Routine monitoring
30-50
NORMAL
Minor deviations
50-65
CAUTION
Increased monitoring
65-80
WARNING
Investigate immediately
80-100
CRITICAL
Emergency response
False Alarm Reduction
Persistence: 3 consecutive readings (15 min) required
Hysteresis: 5-point buffer before alert clears
Result: ~80% fewer false alarms vs raw thresholds

## Slide 5
Probable Cause Identification
Hybrid approach: ML Classifier + Domain Rule Engine + SHAP Explanations
Cause Class
Key Indicators
Typical Duration
Disinfectant Decay
Chloramine drops, THM rises
Hours-days
Contamination/Intrusion
Turbidity spike, conductivity jump
Minutes-hours
Pipe Corrosion
pH drops, hardness rises, conductivity up
Days-weeks
Stagnation
Slow chloramine decay, slight turbidity rise
Hours
Operational Change
Sudden chloramine shift, turbidity stable
Minutes
Sensor Fault
Zero variance detected on sensor readings
Variable
Rule Engine
6 domain-expert rules
Always runs (no model needed)
Provides human-readable
explanations for operators
ML Classifier
LightGBM 7-class model
279 engineered features
Probabilistic output
ranks all possible causes
SHAP Explanations
Per-prediction feature
importance via TreeSHAP
Top-5 contributing factors
shown on dashboard

## Slide 6
Results & Event Detection
0.887
AUC-ROC
Potability Classifier
0.86
F1-macro
Potability Classifier
0.60
Macro-F1
Cause Classifier
0.10
MAE
Chloramine Forecaster
~15 min
Fastest
Time-to- Detect
3 Validated Event Scenarios
Scenario 1: Disinfection Failure
Chloramine drops 4.0 to 0.5 mg/L over 2hrs. Detected at T+40min (WARNING), T+60min (CRITICAL). Cause: 'Disinfectant Decay' -- confidence 85%. Lead time: ~40 min before non-potable.
Scenario 2: Pipe Break Intrusion
Turbidity jumps 2 to 6 NTU, conductivity spikes. Detected at T+15min (WARNING), T+20min (CRITICAL). Cause: 'Contamination Intrusion' -- confidence 80%. Lead time: ~15 min (fast onset).
Scenario 3: Dead-End Stagnation
Overnight chloramine decay in low-flow pipe. Detected at T+6h (CAUTION), T+7h (WARNING). Cause: 'Stagnation' -- confidence 70%. Lead time: ~2 hrs before violation.

## Slide 7
Impact & Next Steps
Public Health Impact
15-40 min early warning before unsafe water reaches consumers
~80% false alarm reduction vs. simple thresholds
Automated root-cause identification saves hours of investigation
5-site monitoring with 5-min granularity (scalable to 100+ sites)
Interpretable explanations build operator trust
Low-cost: runs on standard hardware, open-source stack
Technology Stack
Python | LightGBM | Scikit-learn | SHAP
FastAPI (inference) | Streamlit (dashboard)
Parquet (storage) | Plotly (visualization)
Production Roadmap
Phase 1: Real sensor integration (MQTT / OPC-UA / SCADA)
Phase 2: Weather & demand data fusion for better forecasting
Phase 3: LSTM / Temporal Fusion Transformer for long horizons
Phase 4: Graph Neural Network for pipe network topology
Phase 5: Edge deployment (ONNX on IoT gateways)
Phase 6: Docker + Kubernetes + Azure IoT Hub at scale
AquaGuard -- AI Night Challenge 2026 -- Protecting Public Health with Real-Time AI